Introduction to Mine Engineering			Unit 22	Mine Dewatering

1)  Dewatering a mine deals with not only water but also the ____________________________

2)  What is the function of a "ditch"? ________________________________________________

3)  Ground water flowing into an underground entry (shaft, raise, ramp or adit) is most often

controlled by  ________________________________________________________

4)  What is the function of a sump?_________________________________________________

5) What are slimes? ______________________________________________________________

6) What is a flocculent? ___________________________________________________________

7)  List the 3 classes of underground water :

a) _____________________________________________________________

b) _____________________________________________________________

c) _____________________________________________________________

8) What is "clear water"? __________________________________________________________

9)  What is a "centrifugal pump"? ___________________________________________________

________________________________________________________________

10) What is "dirty water"? __________________________________________________________

________________________________________________________________

11) What causes wear in mine drainage pipes? ________________________________________

12) What does Stoke's Law calculate? ________________________________________________

13) What is the function of a bulkhead? ______________________________________________

________________________________________________________________

14) Which mining method uses considerable amounts of water? _________________________

15) Why are different sand:cement ratios used for sandfill? _____________________________

_______________________________________________________________

16) Why is sandfill preparation necessary? __________________________________________

_______________________________________________________________

Introduction to Mine Engineering			Unit 22	Mine Dewatering

17) What is the purpose of a CATWALK? _____________________________________________

________________________________________________________________

18) Why is burlap used on drain towers? _____________________________________________

________________________________________________________________

19) Why is flocculent added to the sandfill? ___________________________________________

________________________________________________________________

20) What is the purpose of a settling sump? __________________________________________

________________________________________________________________

21) What is a Mars pump? _________________________________________________________

Introduction to Mine Engineering	 Unit 22	Mine Dewatering Answer Sheet

Answer Sheet

1)	Pg. 11		A	B	C	D

2)	Pg. 12		A	B	C	D

3)	Pg. 13		A__	B__	C__	D__

4)	Pg. 20		A	B	C	D

5)	Pg. 21 	A	B	C	D

6)	Pg. 34		T	F

7) 	Pg. 35		A	B	C	D

8)	Pg. 51		A__	B__	C__	D__

9)	Pg. 52		T	F